## Slide 1: CS 0447 Recitation 7

## Slide 2: Last Week’s Quiz
Q1:
  A: Shift right by 11; bitwise AND with 0000000000011111
  We need to get the relevant bits in the right of the bitfield. Then we can bitwise and with a bitmask to extract those bits
Q2:
  A: 01111100
  Remember that IEEE 754 uses biased notation for the exponent – we need to add 127 to get the proper encoding.
Q3:
  A: 224
  As in Q2, the bias constant is 127. We add that to the number being encoded.
Notes: Q1: I have this bitfield: 1011110000010111 and I want to extract the leftmost 5 bits. What is the correct sequence of operations to apply?
Q2: Given you are using IEEE 754 Single-precision or (float). You want to encode the biased exponent for the exponent = -3. What is the encoding?
Q3: For the exponent field, if the exponent is 97, and the bias constant is 127, then what is the biased representation?

## Slide 3: Last Week’s Quiz
Q4:
  A: 1010.1101
  This is a fixed-point number. As with positive binary numbers, we sum up the place values of the positions with 1s. Right of the binary point, the exponents are negative
Q5:
  A: With a fixed size, floats with their decimal point further to the left have more accuracy AND With a fixed size, floats with their decimal point further to the right have more range
  If the decimal point is further left, we are dedicating more bits to the fractional portion of the number and can thus be more precise.
  If the decimal point is further right, we are dedicating more bits to the whole part of the number and can thus represent larger numbers.
Notes: Q4: Which of these is a binary representation of 10.8125?
Q5: Which of the following statements are true?

## Slide 4: This Week’s Quiz
You know the drill: 5 minutes to work on this week’s quiz

## Slide 5: Multiplying in Binary
Remember 3rd grade? You can multiply in binary in the same way
1 times a number is that number, 0 times a number is 0
Line the numbers up and multiply the one on top by the one on the bottom, right to left.
0101
X 0110
------------
0000
01010
010100
0000000 =
00111110

## Slide 6: Multiplying in MIPS
When we multiply two n-bit numbers, the result could be as large as 2n bits
  This is a problem if our registers only hold n bits!
MIPS has two special registers, HI and LO
When you multiply two numbers, the left 32 bits go to HI and the right 32 go to LO
The mul instruction will multiply then move the 32 lower bits into the target register
Notes: Use the mul instruction to multiply

## Slide 7: Signed Multiplication
Nothing really changes when dealing with signed numbers
As you’d expect, the result is negative when the signs don’t match and positive otherwise

## Slide 8: Division in Binary
What is division?
  We’re basically trying to figure out how many times a number can fit into another number
In binary, the same holds true
We can also divide in binary using the same long-division thing you learned in elementary school

## Slide 9: Multiplication in binary is easy, which simplifies division
1001001
1100
1100≤1?
1100≤10?
1100≤100?
-1100
110
0
-1100
0
1100≤1001?
1100≤10010!
R1
0
0
0
0
1
1
1
0
1100≤1100!
1100≤1?
in binary, each step becomes a yes-no choice: does the divisor fit into the remainder?
Notes: I yoinked this slide from the professor lol

## Slide 10: Division in MIPS
As with multiplication, MIPS will make use of the HI and LO registers for division
The remainder goes in HI and the quotient goes in LO
The div instruction will divide two numbers and then move the quotient into the target register

## Slide 11: Efficiency of Multiplication
Multiplication is just a bunch of repeated additions
  Remember how we added up the results of the smaller multiplications?
Since multiplication is communitive, those additions can be done in any order
  Therefore, we can parallelize multiplication and get an O(log(N)) runtime, where N is the number of bits in the numbers being multiplied

## Slide 12: Efficiency of Division
Division can be thought of as repeated subtraction
Unfortunately, subtraction is not communitive and thus we cannot parallelize it 
  Each step depends on the output of the previous step
This means that division on a computer is inherently slower than multiplication

## Slide 13: Lab 7 Part A
This lab is very important!! It will prepare you for Project 2!
  When I took 447 this lab was a big help for the second project
A.2 – Look at the draw_horizontal_line implementation – this is almost the same except the line needs to be vertical
A.3 – You are given a Java implementation of this function
  You’ve translated code into MIPS before – this is the same thing
Notes: A.1: Read through professor’s code
A.2: Implement a function to draw a vertical line
A.3: Implement function to draw a spiral, Java implementation is provided

## Slide 14: Lab 7 Part B – Game Development
Games (and interactive programs generally) follow a pattern
  Check for input
  Update the parts of the game that have changed
  Display everything on the screen
  Wait for the next frame
    A frame is one step in the game
    This is where the term “frame rate” comes from

## Slide 15: Lab 7 Part B – Model-View-Controller
Model, View, Controller (MVC) is a common way to organize a program
The way your program looks, how the user interacts with it, and its internal representation should be separate
Model – The program’s internal state
  Variables, arrays, etc
View – What the user sees
Controller – How the view is changed
  Either by your code or by the user
This is a very useful way to organize a program

## Slide 16: Lab 7 Part B – “Objects” in MIPS
If we want to represent a pixel in our program, it needs some attributes
  x position, y position, color
We could just declare a variable for each attribute
But if we want multiple pixels, we’d need a bunch more variables
Solution: create an array of words
  Every 3 words is a pixel object
  We use .eqv directives to easily index into the array
The lab description talks about the above in more detail
Notes: We won’t cover dynamic memory allocation, so you’ll still need to allocate the array ahead of time

## Slide 17: Lab 7 Part B – Implementation
The enter and leave macros handle pushing/popping for you
  Pass the s registers you want to save as arguments (ie save s0, s1, s2)
B.1 – There is a comment explaining how the function should proceed
  The array of pixels is defined in pixel_model.asm
  Make use of display_set_pixel from display.asm
    Include that file and jal the function as normal
  For checking if the pixel is selected – look at pixel_struct.asm to get the offsets needed to check that field
B.2 – Again, look at the comment
  You can move the pixel by changing its x and y values
  The input is the current frame – use this to tell if the selected pixel should change
  There is an action_pressed variable to check if b was pressed
Notes: B.1 – implement pixel_draw
B.2 – Implement pixel_update