## Slide 1: CS 447 Recitation 8

## Slide 2: Announcements
Project 2 is out!
You need to have a planning meeting with me by Tuesday the 9th
  Don’t throw away 10 easy points!

## Slide 3: Last Week’s Quiz
Q1:
  A: The last two options.
  If the result is negative, there are 1s in HI, and MSB of LO is 0 -> overflow
Q2:
  A: div followed by mflo
  div is a pseudo-op. It expands into the above two instructions so that the quotient can easily be placed into the target register
Notes: Q1: Detect which of the following scenarios below have resulted in 32-bit signed multiplication overflow. Examine the values in the HI and LO registers (Select all that apply)
Q2: What operation does the div instruction actually perform?

## Slide 4: Last Week’s Quiz
Q3
  A: In MIPS, the values of the HI & LO registers are changed when we call either mult or mul AND Multiplication is much faster than Division because its operations could be broken down and run in parallel
  The MIPS ISA will change the values of HI and LO when a multiplication is preformed, regardless of whether mult or mul was called. Multiplication can be parallelized to run in O(log(N)) time, whereas division cannot be parallelized and runs in O(N) time
Q4:
  A: HI
  MIPS places the remainder in HI and the quotient in LO
Notes: Q3: Which of the following statements are true?
Q4: When dividing in MIPS, where can you find the remainder?

## Slide 5: This Week’s Quiz
5 minutes to work on the quiz as per usual

## Slide 6: Transistors
A transistor is like a little valve that electricity flows through
We will focus on MOSFET transistors
They come in two varieties – N and P
N type – Electricity will flow through when the input is 1
P type – Electricity will flow through when the input is 0

## Slide 7: Gates
We can combine transistors to make gates
  Then we can combine a load of gates to make a computer
A gate implements one of the basic boolean logic functions (NOT, OR, AND, etc)

## Slide 8: Not Gate
This is the simplest gate
It simply inverts the input
We can create a NOT gate by combining an N and a P type MOSFET transistor
A
Q
A | Q
0 | 1
1 | 0

## Slide 9: NAND, AND, OR, NOR
We can also create these gates using MOSFETs
You’re probably familiar with how the boolean truth tables would work for each of these
  The truth table is identical when thinking about the logic gates
A
Q
B
A
Q
B
A
Q
B
A
Q
B
NAND
AND
OR
NOR

## Slide 10: New Logic Gate Just Dropped
You’re might not be familiar with this one – it’s an XOR gate
That stands for eXclusive or
It means that one of the inputs must be 1, but not both
A
Q
B
XOR gate
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 11: Combining Logic Gates
If we want to simulate more complex expressions, we just connect logic gates together
For example: (A and B) OR (not C)
Create an AND gate for A and B
A
B

## Slide 12: Combining Logic Gates
If we want to simulate more complex expressions, we just connect logic gates together
For example: (A and B) OR (not C)
Create a NOT gate for not C:
C

## Slide 13: Combining Logic Gates
If we want to simulate more complex expressions, we just connect logic gates together
For example: (A and B) OR (not C)
Connect them with an OR gate
A
B
C
AB
Q
~C

## Slide 14: Adding Circuits
We want to create a circuit that can add numbers
  3 steps:
  Create a truth table that represents adding
  Turn that table into a logic function
  Turn that logic function into a circuit

## Slide 15: Adding Longer Numbers
We might get a carry out when adding bits in a given place
That becomes the carry in for the next place to the left
So to add n-bit numbers, we connect n one bit adders by hooking up their carry-out outputs and carry-in inputs
However – gate delay
  Each bit must wait for the smaller bit to compute its carry-out value
  So we get a delay that is linear in the number of bits
  There are more efficient ways of adding

## Slide 16: Subtracting
There is no need for a separate subtraction circuit – just add a negative
How? Flip the bits and add one
  We can flip the bits using NOT gates
  We can add one by setting the carry-in to 1 when subtracting

## Slide 17: Detecting Overflow
For unsigned addition
  Look at the carry-out of the MSB – if it’s 1, there is overflow
For signed addition
  Look at the last carry-in and carry-out – if they are different, there is overflow

## Slide 18: Multiplexers
We want to our hardware to make decisions
A multiplexer (mux) outputs one of its inputs based on a select
Notes: Multiple inputs, one output

## Slide 19: Demultiplexers
A demultiplexer (demux) does the opposite of a mux
It sends its input to one of its outputs
Notes: One input, multiple outputs

## Slide 20: Encoders
An encode turns 2n inputs into n outputs
That is, you give it a bunch of 1-bit inputs, and it’ll tell you which one is 1
Note: exactly one input must be 1, otherwise the output is invalid
Enc
1
0
0
0
0
0
0
1
2
3
0
1
Enc
1
0
0
0
1
0
0
1
2
3
0
1
Enc
0
0
0
0
???
???
0
1
2
3
0
1
0
valid

## Slide 21: Priority Encoders
We can fix that issue using priority encoders
These will tell you which of the inputs is the highest with a 1
So you can have multiple inputs be 1
All 0s is still invalid, however
Pri
1
1
0
0
0
1
0
1
2
3
0
1
Pri
0
0
0
0
X
X
0
1
2
3
0
1
0
valid

## Slide 22: Decoder
A decoder is the opposite of an encoder
It has multiple outputs
The output corresponding to the value of the select input is a 1, and all others are 0
Example: the select input is 0, so the 0’th output is 1

## Slide 23: Project 2
This project is a game!
It’s basically the game Millipede that you might’ve seen in an arcade
Gameplay overview:
  A millipede starts at the top of the screen and crawls towards the bottom
  There are mushrooms on the screen that block the millipede’s path
  The player shoots at the millipede
    If a section is destroyed, it turns into a mushroom

## Slide 24: The Arena
The display in MARS is 64 by 64 pixels
It should be divided into two parts – The upper section where gameplay happens and the lower section where information is displayed
Bottom part
  Designate some section of the 64x64 grid as the “bottom part”
  You should have some variables to store the number of points and lives
  Use the provided functions to display these values
Top part
  The other part of the grid is the top part
  Mushrooms, millipede segments, and the player are all 5x5 squares
  You need to know whether a given coordinate has a mushroom – maybe use a matrix?

## Slide 25: Displaying Things
The mushrooms, millipede segments, and player are all 5x5 pixels
  The project description refers to things of this size as “blits”
  They are represented as 5x5 matrices of bytes
  Use the display_blit_5x5 to draw the millipedes and mushrooms
  Use display_blit_5x5_trans to draw the player
There are also built in functions to draw lines, numbers, and text
Use the functions provided to you!

## Slide 26: The Player
The player can be moved with the arrow keys, and can shoot with the ‘b’ button
Make sure you check for collisions with the arena bounds so the player can’t move offscreen
Remember MVC: what do you need to keep track of for the player?
  X coordinate, y coordinate, points, lives, appearance, etc
Follow the hints/steps given in the project description
Write small bits of code at a time and test
Notes: Same idea as in Lab 7!

## Slide 27: The Millipedes
When the game starts, there should be a millipede consisting of at least 5 segments
It will move horizontally until it either hits an edge or a mushroom, in which case it moves downwards one row
  You can ignore mushrooms when moving down
If the millipede gets shot
  The segment that was shot turns into a mushroom
  The millipede splits in two
If the millipede hits the bottom
  The player loses a life
  The millipede despawns and reappears at the top

## Slide 28: Representing the Millipedes
You’ll need some way to represent the millipedes in memory
  I would use an array of structs (Lab 7!) but you don’t have to
Think about what information on each segment needs to be stored
  Position, whether it’s a head, etc
Follow along with the implementation hints in the project description

## Slide 29: The Bullet
When the player shoots:
  A bullet appears in the same block as the player
  It moves upwards until it hits something or reaches the top of the screen
    If it hits a mushroom: Remove the mushroom
    If it his the millipede: That segment is destroyed; millipede splits
After the bullet either hits something or reaches the top, it should despawn

## Slide 30: Starting and Ending the Game
When the game starts, wait for the player to press a key
  Check out the input_get_keys_pressed function
The game ends when the player runs out of lives
Once the game is over, display the player’s score

## Slide 31: General Tips
Write small pieces and then test
Split your code up
  Divide your program into multiple files – when I did this project the model, view, and controller for each element were their own files
  Divide files into functions
    Each function should do a single thing
    Split big functions into smaller functions!
Use the model-view-controller paradigm
Plan out code before you write it
The project description has a ton of hints – follow them. You should also follow along with the suggested project stages

## Slide 32: Lab 8 Part A
Make sure you have Logisim downloaded and that it works
  If you’re having trouble, talk to me
This part of the lab will introduce you to the Logisim software
You’re given the circuit diagram for a one-bit adder. All you need to do is follow along with the directions and implement it

## Slide 33: Lab 8 Part B
You’re given a truth table and a boolean expression that you need to turn into a circuit
What you submit does not need to be optimal as long as it works correctly
  It still wouldn’t hurt to think of ways you might shrink the circuit
We talked about combining gates to form more complex circuits – that’s what you need to do here

## Slide 34: Lab 8 Part C
You have the adder circuit from part A
Change the input pins and fill out the table based on what you see
All you need to do is try all the different values for A, B, and C_in and see what the value of each gate is